## Slide 1
Chapter 1
Introduction

## Slide 2
Processor Trends
Source: M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, C. Batten (1970-2010 ). K. Rupp (2010-2017).
Chart: 
Transistors (thousands)
100
101
102
103
104
105
106
107
108
Moore’s “Law” predicted that the number of transistors per unit area would double every 18-24 months

## Slide 3
Processor Trends
Source: M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, C. Batten (1970-2010 ). K. Rupp (2010-2017).
Chart: 
Transistors (thousands)
Frequency
(MHz)
100
101
102
103
104
105
106
107
108
Processor frequency (clock rate) followed the same trend because smaller transistors can be switched faster… until around 2005.

## Slide 4
Processor Trends
Source: M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, C. Batten (1970-2010 ). K. Rupp (2010-2017).
Chart: 
Transistors (thousands)
Frequency
(MHz)
Typical Power
(Watts)
100
101
102
103
104
105
106
107
108
Around 2005, frequency stopped increasing due to the power wall (increasing frequency further would make the chip too hot to cool feasibly)

## Slide 5
Processor Trends
Source: M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, C. Batten (1970-2010 ). K. Rupp (2010-2017).
Chart: 
Transistors (thousands)
Frequency
(MHz)
Typical Power
(Watts)
100
101
102
103
104
105
106
107
108
Single-thread Performance (SpecINT x 103)
Stagnation in frequency led to a stagnation in single-thread performance, except for some improvements due to architecture and compiler advancements

## Slide 6
Processor Trends
Source: M. Horowitz, F. Labonte, O. Shacham, K. Olukotun, L. Hammond, C. Batten (1970-2010 ). K. Rupp (2010-2017).
Chart: 
Transistors (thousands)
Frequency
(MHz)
Typical Power
(Watts)
100
101
102
103
104
105
106
107
108
Number of Logical Cores
Single-thread Performance (SpecINT x 103)
Stagnation in single-thread performance made parallel computing mainstream as transistors were invested in adding more cores to processors

## Slide 7
Design Approaches
Minimize the time it takes to perform a single task
Maximize the number of tasks that can be performed in a given time frame
Latency-Oriented Design
Throughput-Oriented Design

## Slide 8
Processor Design Approaches
A few powerful ALUs
  Reduced operation latency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction to reduce control hazards
  Data forwarding to reduce data hazards
Modest multithreading to hide short latency
High clock frequency
Many small ALUs
  Long latency, high throughput
  Heavily pipelined for further throughput
Small caches
  More area dedicated to computation
Simple control
  More area dedicated to computation
Massive number of threads to hide the very high latency!
Moderate clock frequency
Cache
ALU
Control
ALU
ALU
ALU
CPU: Latency-Oriented Design
GPU: Throughput-Oriented Design

## Slide 9
GPU Origins
GPUs were originally built for graphics
  Hence the name, Graphics Processing Unit
  Graphics workloads process a massive number of pixels in parallel
Before 2007, the only way to program GPUs was using graphics APIs
  e.g., OpenGL, Direct3D
  Using GPUs for other than graphics meant reformulating a computation as a function that paints a pixel
In 2007, NVIDIA released CUDA
  A programming interface for using GPUs in a general purpose way
  Requires extensions to the GPU architecture

## Slide 10
Source: Jensen Huang, GTC’15 Keynote
Source: Jensen Huang, GTC’19 Keynote
Growth of GPU Computing

## Slide 11
Top Supercomputers
GPU accelerated computers in 2020:
  #1 in USA, #2 worldwide – Summit
  #1 in Europe, #8 worldwide – Juwels
  7 out of the top 10 supercomputers worldwide
  #2 in energy-efficient supercomputers (Green500)
  9 out of top 10 energy-efficient supercomputers
Source: top500.org, November 2021

## Slide 12
Why GPUs?
Chips are expensive to build and require a large volume of sales to amortize the cost
  This makes the chip market very difficult to penetrate
When parallel computing became mainstream, GPUs already had (and still have) a large installed base from the gaming sector
  Gave them a head start compared to other potential massively parallel accelerators

## Slide 13
GPU Market Sector Breakdown
Chart: 
| Other | Automotive | Professional Visualization | Datacenter | Gaming
 | 116 | 161 | 281 | 760 | 1805
Source: NVIDIA, Q2 FY19
Revenue from Different Market Sectors
Breakdown of Datacenter Sector
Source: NVIDIA, 2018

## Slide 14
Parallel Programming Frameworks
In this class, we will focus on CUDA
Other GPU parallel programming frameworks:
  OpenCL
  OpenACC
Popular CPU programming frameworks
  MPI (distributed memory system)
  OpenMP (shared memory system)
  Both can be used in conjunction with CUDA

## Slide 15
Parallel Computing Pitfall
Consider an application where:
  The sequential execution time is 100s
  The fraction of execution that is parallelizable is 90%
  The speedup achieved on the parallelizable part is 1000×
What is the overall speedup of the application?

## Slide 16
Amdahl’s Law
In general, if an application has:
  t sequential execution time
  p fraction of execution that is parallelizable
  s speedup achieved on the parallelizable part
What is the overall speedup of the application?

## Slide 17
Amdahl’s Law Implications
The maximum speedup of a parallel program is limited by the fraction of execution that is parallelizable
  e.g., if p is 90%, speedup < 10×
Fortunately, for many real applications, p > 99% especially for large datasets, and speedups >100× are attainable

## Slide 18
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.