## Slide 1
Chapter 2
Heterogeneous Data Parallel Computing

## Slide 2
Task Parallelism
Different operations performed on same or different data
Usually a modest number of tasks unleashing a modest amount of parallelism
Data Parallelism
Same operations performed on different data
Potentially massive amounts of data unleashing massive amounts of parallelism
  Most suitable for GPUs
Types of Parallelism
Task A
Task C
Task B
Data 1
Data 2
Task A
Data 1
Task A
Data 2
Task A
Data 3
Task A
Data 4
Task A
Data 5

## Slide 3
Vector Addition
Vector addition
  The “Hello, World!” for data parallel programming
Input Vector x:
Input Vector y:
Output Vector z:
+
=
void vecadd(float* x, float* y, float* z, int N) {
for(unsigned int i = 0; i < N; ++i) {
z[i] = x[i] + y[i];
}
}
Sequential C Code

## Slide 4
System Organization
CPU
(also called the host)
GPU
(also called the device)
Main Memory
(also called host memory)
GPU Memory
(also called device memory)
The CPU and GPU have separate memories can cannot access each others’ memories
Need to transfer data between them

## Slide 5
Memory Management
CPU
GPU
Main Memory
GPU Memory
❶ Allocate GPU memory
❷ Copy data to GPU memory
❸ Perform computation on GPU
❹ Copy data from GPU memory
❺ Deallocate GPU memory
❷
❸
❹
❶
❺

## Slide 6
CUDA Memory Management API
Allocating memory:
  cudaError_t cudaMalloc(void **devPtr, size_t size)
  devPtr: Pointer to pointer to allocated device memory
  size: Requested allocation size in bytes
Deallocating memory:
  cudaError_t cudaFree(void *devPtr)
  devPtr: Pointer to device memory to free
Return type: cudaError_t
  Helps with error checking (discussed later)

## Slide 7
CUDA Memory Management API
Copying memory:
  cudaError_t cudaMemcpy(void *dst, const void *src, size_t count, enum cudaMemcpyKind kind)
  dst: Destination memory address
  src: Source memory address
  count: Size in bytes to copy
  kind: Type of transfer
    cudaMemcpyHostToHost
    cudaMemcpyHostToDevice
    cudaMemcpyDeviceToHost
    cudaMemcpyDeviceToDevice

## Slide 8
Code Example
void vecadd(float* x, float* y, float* z, int N) {
// Allocate GPU memory
float *x_d, *y_d, *z_d;
cudaMalloc((void**) &x_d, N*sizeof(float));
cudaMalloc((void**) &y_d, N*sizeof(float));
cudaMalloc((void**) &z_d, N*sizeof(float));
// Copy data to GPU memory
cudaMemcpy(x_d, x, N*sizeof(float), cudaMemcpyHostToDevice);
cudaMemcpy(y_d, y, N*sizeof(float), cudaMemcpyHostToDevice);
// Perform computation on GPU
...
// Copy data from GPU memory
cudaMemcpy(z, z_d, N*sizeof(float), cudaMemcpyDeviceToHost);
// Deallocate GPU memory
cudaFree(x_d);
cudaFree(y_d);
cudaFree(z_d);
}

## Slide 9
Parallel Vector Addition
Simple strategy: assign one GPU thread per vector element
Input Vector x:
Input Vector y:
Output Vector z:

## Slide 10
Grids
An array of GPU threads is called a grid

## Slide 11
Blocks
Threads in a grid are grouped into thread blocks
(significance: threads in the same block can collaborate in ways that threads in different blocks cannot – discussed later)

## Slide 12
Launching a Grid
Threads in the same grid execute the same function known as a kernel
A grid can be launched by calling a kernel and configuring it with appropriate grid and block sizes
  Example:
const unsigned int numThreadsPerBlock = 512;
const unsigned int numBlocks = N/numThreadsPerBlock;
vecadd_kernel <<< numBlocks, numThreadsPerBlock >>> (x_d, y_d, z_d, N);

## Slide 13
Implementing a Kernel
A kernel is similar to a C/C++ function
It is preceded by the keyword __global__ to indicate that it is a GPU kernel
It uses special keywords to distinguish different threads from each other

## Slide 14
Grid Dimension
gridDim.x
# of blocks in grid

## Slide 15
Block Index
gridDim.x
blockIdx.x
# of blocks in grid
position of block in grid

## Slide 16
Block Dimension
gridDim.x
blockIdx.x
blockDim.x
# of blocks in grid
position of block in grid
# threads in block

## Slide 17
Thread Index
gridDim.x
blockIdx.x
blockDim.x
threadIdx.x
# of blocks in grid
position of block in grid
# threads in block
position of thread in block

## Slide 18
Parallel Vector Addition in CUDA
Input Vector x:
Input Vector y:
Output Vector z:
__global__ void vecadd_kernel(float* x, float* y, float* z, int N) {
int i = blockDim.x*blockIdx.x + threadIdx.x;
z[i] = x[i] + y[i];
}
Identify a thread’s global index and use it to index the arrays

## Slide 19
Boundary Conditions
Recall launch configurations:
If N is not a multiple of numThreadsPerBlock, fewer threads will be launched than desired
Solution: use the ceiling to launch extra threads then omit the threads after the boundary
const unsigned int numThreadsPerBlock = 512;
const unsigned int numBlocks = N/numThreadsPerBlock;
vecadd_kernel <<< numBlocks, numThreadsPerBlock >>> (x_d, y_d, z_d, N);

## Slide 20
Execution with Boundary Checks
Input Vector x:
Input Vector y:
Output Vector z:

## Slide 21
Code with Boundary Checks
Launch code:
Kernel code
const unsigned int numBlocks = (N + numThreadsPerBlock – 1)/numThreadsPerBlock;
__global__ void vecadd_kernel(float* x, float* y, float* z, int N) {
int i = blockDim.x*blockIdx.x + threadIdx.x;
if(i < N) {
z[i] = x[i] + y[i];
}
}

## Slide 22
Compilation
C/C++ and CUDA code
NVIDIA CUDA Compiler (NVCC)
Host C/C++ Compiler
Host C/C++ Code
PTX (Virtual) ISA code
Device Just-in-Time Compiler
Device Assembly
(e.g., SASS)
Host Assembly
(e.g., x86, Power, ARM)
.cu
.ptx
.c
CPU
GPU

## Slide 23
Function Declarations
Keywords that differentiate where a function is intended to run
Why need __host__ if it is the default?
Keyword | Callable From | Executed On
__host__ (default) | Host | Host
__global__ | Host (or Device) | Device
__device__ | Device | Device

## Slide 24
Function Declarations
The keyword __host__ is useful when needing to mark a function as executable on both the host and the device
__host__ __device__ float f(float a, float b) {
return a + b;
}
void vecadd(float* x, float* y, float* z, int N) {
for(unsigned int i = 0; i < N; ++i) {
z[i] = f(x[i], y[i]);
}
}
__global__ void vecadd_kernel(float* x, float* y, float* z, int N) {
int i = blockDim.x*blockIdx.x + threadIdx.x;
if (i < N) {
z[i] = f(x[i], y[i]);
}
}

## Slide 25: How much faster?

## Slide 26
Asynchronous Kernel Calls
By default, kernel calls are asynchronous
  Useful for overlapping GPU computations with CPU computations
Use the following API function to synchronize
  cudaError_t cudaDeviceSynchronize()
  Blocks until the device has completed all preceding requested tasks

## Slide 27
Error Checking
All CUDA API calls return an error code cudaError_t that can be used to check if any errors occurred
  Example:
For kernel calls, one can check the error returned by cudaDeviceSynchronize() or call the following API function:
  cudaError_t cudaGetLastError()
cudaError_t err = ...;
if(err != cudaSuccess) {
printf("Error: %s\n", cudaGetErrorString(err));
exit(0);
}

## Slide 28
You just learned CUDA!
The rest of this course is about parallelization strategies and optimizations for massively parallel processors

## Slide 29
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.
CUDA C++ Programming Guide: https://docs.nvidia.com/cuda/cuda-c-programming-guide