## Slide 1
Chapter 10
Reduction

## Slide 2
Reduction
A reduction operation reduces a set of input values to one value
  e.g., sum, product, min, max
Reduction operations are:
  Associative
  Commutative
  Have a well-define identity value
We will use sum as an example

## Slide 3
Sequential Reduction
Sequential reduction for sum:
In general:
sum = 0.0f;
for(i = 0; i < N; ++i) {
sum += input[i];
}
acc = IDENTITY;
for(i = 0; i < N; ++i) {
acc = f(acc, input[i]);
}

## Slide 4
Parallel Reduction with Atomics
Parallel reduction for sum using atomics:
Poor performance:
  All additions are serialized by the hardware
unsigned int i = blockIdx.x*blockDim.x + threadIdx.x;
if(i < N) {
atomicAdd(sum, input[i]);
}

## Slide 5
Parallel Reduction
4
7
2
3
8
5
9
6
11
5
13
15
+
+
+
+
+
+
16
28
+
44
Approach: Every thread adds two elements in each step
Takes log(N) steps and half the threads drop out every step
Pattern is called a reduction tree

## Slide 6
Segmented Reduction
Threads must synchronize between steps
  Cannot synchronize across threads in different blocks
Solution: segmented reduction
  Every thread block reduces a segment of the input and produces a partial sum
  The partial sum is atomically added to the final sum

## Slide 7
Segmented Reduction Example
Input
Segment0
Segment1
SegmentB-1
…
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Block0
Block1
BlockB-1
Sum

## Slide 8
Reduction Tree (Per Block)

## Slide 9
Reduction Code
Problems:
  Accesses to input are not coalesced
  Control divergence
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + 2*threadIdx.x;
for(unsigned int stride = 1; stride <= BLOCK_DIM; stride *= 2) {
if(threadIdx.x%stride == 0) {
input[i] += input[i + stride];
}
__syncthreads();
}

## Slide 10
Control Divergence Problem
warp 0
warp 1
warp 2
warp 3
Step N-2
Step N-3
Step N-4
Step N-1
drops out
drops out
Step N
drops out

## Slide 11
Coalescing and Minimizing Divergence

## Slide 12
Control Divergence Minimized
warp 0
warp 1
warp 2
warp 3
Step N-4
Step N-1
Step N
Step N-3
drops out
drops out
Step N-2
drops out

## Slide 13
Reduction Code with Coalescing and Minimizing Divergence
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
for(unsigned int stride = BLOCK_DIM; stride > 0; stride /= 2) {
if(threadIdx.x < stride) {
input[i] += input[i + stride];
}
__syncthreads();
}

## Slide 14
Data Reuse
While specific data values are not reused, the same memory locations are repeatedly read and written
Optimization: load input to shared memory first and perform reduction tree on shared memory
  Also avoids modifying the input if needed in the future

## Slide 15
Using Shared Memory
Initial load from global memory
Subsequent writes and reads continue in shared memory

## Slide 16
Reduction Code with Shared Memory
unsigned int segment = 2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
// Load data to shared memory
__shared__ float input_s[BLOCK_DIM];
input_s[threadIdx.x] = input[i] + input[i + BLOCK_DIM];
__syncthreads();
// Reduction tree in shared memory
for(unsigned int stride = BLOCK_DIM/2; stride > 0; stride /= 2) {
if(threadIdx.x < stride) {
input_s[threadIdx.x] += input_s[threadIdx.x + stride];
}
__syncthreads();
}

## Slide 17
Thread Coarsening
Cost of parallelization:
  Synchronization every step
  Control divergence in the final steps
Better to coarsen threads if there are many more blocks than resources available

## Slide 18
Applying Thread Coarsening

## Slide 19
Before vs. After Coarsening
Hardware fully utilized
Hardware underutilized
Hardware fully utilized
Hardware underutilized
Hardware fully utilized
Execution of two non-coarsened thread blocks serialized by the hardware
Execution of one coarsened thread block doing the work of two original non-coarsened thread blocks
Hardware underutilized

## Slide 20
Reduction Code with Thread Coarsening
unsigned int segment = COARSE_FACTOR*2*blockDim.x*blockIdx.x;
unsigned int i = segment + threadIdx.x;
// Load data to shared memory
__shared__ float input_s[BLOCK_DIM];
float threadSum = 0.0f;
for(unsigned int c = 0; c < COARSE_FACTOR*2; ++c) {
threadSum += input[i + c*BLOCK_DIM];
}
input_s[threadIdx.x] = threadSum;
__syncthreads();
// Reduction tree in shared memory
for(unsigned int stride = BLOCK_DIM/2; stride > 0; stride /= 2) {
if(threadIdx.x < stride) {
input_s[threadIdx.x] += input_s[threadIdx.x + stride];
}
__syncthreads();
}

## Slide 21
Coarsening Benefits
Let N be the number of elements per original block
  i.e., N = 2*blockDim.x
If blocks are all executed in parallel:
  log(N) steps, log(N) synchronizations
If blocks serialized by the hardware by a factor of C:
  C*log(N) steps, C*log(N) synchronizations
If blocks are coarsened by a factor of C:
  2*(C – 1) + log(N) steps, log(N) synchronizations

## Slide 22
Boundary Conditions
Do not load and add out-of-bounds values

## Slide 23
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.