## Slide 1
Chapter 8
Stencil

## Slide 2
Stencil
The stencil computation pattern refers to a class of computations on a grid where the value at a grid point is computed based on neighboring points
  Typically used in solving partial differential equations in domains such as fluid dynamics, heat conductance, combustion, weather forecasting, etc.
Example:
5-point stencil (2D)
7-point stencil (3D)

## Slide 3
Stencil (5-point, 2D)
Grid of points:
(4x4 grid shown)
Stored as 2D array:
(16x16 grid shown)
Input
Output
The output value is computed based on the corresponding and neighboring input values

## Slide 4
Stencil (7-point, 3D)
Grid of points:
(one stencil shown)
Stored as 3D array:
(8x8x8 grid shown)
Input
Output
The output value is computed based on the corresponding and neighboring input values

## Slide 5
Parallelizing Stencil (2D)
Grid of points:
(4x4 grid shown)
Stored as 2D array:
(16x16 grid shown)
Input
Output
Parallelization Approach:
Assign one thread per output grid point
(use 2D grid of threads)

## Slide 6
Boundary Conditions
Grid of points:
(4x4 grid shown)
Stored as 2D array:
(16x16 grid shown)
Input
Output
Only compute internal output values such that all input values are in bounds
(input values at the boundary typically store boundary conditions)

## Slide 7
Parallelizing Stencil (3D)
Grid of points:
(one stencil shown)
Stored as 3D array:
(8x8x8 grid shown)
Input
Output
i
j
k
N
N
N
Parallelization Approach:
Assign one thread per output grid point
(use 3D grid of threads)

## Slide 8
Stencil Code
#define BLOCK_DIM 8
__global__ void stencil_kernel(float* in, float* out, unsigned int N) {
unsigned int i = blockIdx.z*blockDim.z + threadIdx.z;
unsigned int j = blockIdx.y*blockDim.y + threadIdx.y;
unsigned int k = blockIdx.x*blockDim.x + threadIdx.x;
if(i >= 1 && i < N - 1 && j >= 1 && j < N - 1&& k >= 1 && k < N - 1) {
out[i*N*N + j*N + k] = C0*in[i*N*N + j*N + k]
+ C1*in[i*N*N + j*N + (k - 1)]
+ C2*in[i*N*N + j*N + (k + 1)]
+ C3*in[i*N*N + (j - 1)*N + k]
+ C4*in[i*N*N + (j + 1)*N + k]
+ C5*in[(i - 1)*N*N + j*N + k]
+ C6*in[(i + 1)*N*N + j*N + k];
}
}

## Slide 9
Data Reuse in Stencil (2D)
output
input
(in global memory)
Observation: Threads in the same block load some of the same input elements

## Slide 10
Shared Memory Tiling (2D)
output
Observation: Threads in the same block load some of the same input elements
Optimization: Each thread loads one input element to shared memory and other threads access the element from shared memory
inputtile
(in shared memory)

## Slide 11
Different Tile Dimensions
Challenge: Input and output tiles have different dimensions
( output tile dimension = input tile dimension – 2 )
Solution: Launch enough threads per block to load the input tile to shared memory, then use a subset of them to compute and store the output tile
output tile dimension
input tile dimension
inputtile
(in shared memory)
output

## Slide 12
Different Tile Dimensions
thread block
output tile dimension
input tile dimension
inputtile
(in shared memory)
input tile dimension
output

## Slide 13
Different Tile Dimensions
thread block
output tile dimension
input tile dimension
inputtile
(in shared memory)
input tile dimension
all threads active when loading the input tile
output

## Slide 14
Different Tile Dimensions
thread block
output tile dimension
input tile dimension
inputtile
(in shared memory)
input tile dimension
output tile dimension
only internal threads active when computing and storing the output tile
output

## Slide 15
Data Reuse in Stencil (3D)
output
input
(in global memory)

## Slide 16
Shared Memory Tiling
output
inputtile
(in shared memory)

## Slide 17
Stencil with Shared Memory Tiling Code
#define BLOCK_DIM 8
#define IN_TILE_DIM BLOCK_DIM
#define OUT_TILE_DIM (IN_TILE_DIM - 2)
__global__ void stencil_kernel(float* in, float* out, unsigned int N) {
int i = blockIdx.z*OUT_TILE_DIM + threadIdx.z - 1;
int j = blockIdx.y*OUT_TILE_DIM + threadIdx.y - 1;
int k = blockIdx.x*OUT_TILE_DIM + threadIdx.x - 1;
__shared__ float in_s[IN_TILE_DIM][IN_TILE_DIM][IN_TILE_DIM];
if(i >= 0 && i < N && j >= 0 && j < N && k >= 0 && k < N) {
in_s[threadIdx.z][threadIdx.y][threadIdx.x] = in[i*N*N + j*N + k];
}
__syncthreads();
if(i >= 1 && i < N - 1 && j >= 1 && j < N - 1 && k >= 1 && k < N - 1) {
if(threadIdx.z >= 1 && threadIdx.z < IN_TILE_DIM - 1 && threadIdx.y >= 1
&& threadIdx.y < IN_TILE_DIM - 1 && threadIdx.x >= 1 && threadIdx.x < IN_TILE_DIM - 1) {
out[i*N*N + j*N + k] = C0*in_s[threadIdx.z][threadIdx.y][threadIdx.x]
+ C1*in_s[threadIdx.z][threadIdx.y][threadIdx.x - 1]
+ C2*in_s[threadIdx.z][threadIdx.y][threadIdx.x + 1]
+ C3*in_s[threadIdx.z][threadIdx.y - 1][threadIdx.x]
+ C4*in_s[threadIdx.z][threadIdx.y + 1][threadIdx.x]
+ C5*in_s[threadIdx.z - 1][threadIdx.y][threadIdx.x]
+ C6*in_s[threadIdx.z + 1][threadIdx.y][threadIdx.x];
}
}
}

## Slide 18
Arithmetic to Global Memory Access Ratio
Original kernel:
  Each thread performs 13 OPs (6 FP adds and 7 FP muls)
  Each thread loads 28 B from global memory (7 FP values)
  Ratio: (13 OPs)/(28 B) = 0.46 OP/B
Tiled kernel:
  Assume the input tile size is T (output tile size is T – 2)
  Each block performs (13 OPs)*(T – 2)3 = 13(T – 2)3 OPs
  Each block loads (4 B)*T3
  Ratio: [13*(T – 2)3]/[4*T3] = 3.25*(1 – 2/T)3
    For T=8, the ratio is 1.37 OP/B
    Increasing T will improve the ratio
      For T=32, ratio is 2.68 (≈2× improvement)
      Intuition: boundary elements have lower data reuse, and increasing tile size decreases the ratio of boundary elements to total elements

## Slide 19
Small Tile Size
output
inputtile
(in shared memory)

## Slide 20
Large Tile Size
output
inputtile
(in shared memory)
Fewer boundary elements relative to internal elements

## Slide 21
Increasing Input Tile Size
Challenges with increasing input tile size:
  Block size limit: The input tile size in the current implementation is the same as the block size which is limited by the hardware
  Shared memory capacity limit: The input tile size in the current implementation determines the shared memory usage per block which is limited by hardware
    Even if the limit is not exceeded, using too much shared memory may hurt occupancy
Solutions:
  Block size limit: Use thread coarsening to process a larger input/output tile without using more threads
    Price of parallelization here is redundant loading of boundary elements
  Shared memory capacity limit: Only keep needed slices of the input tile in shared memory

## Slide 22
Limits Exceeded
output
inputtile
(in shared memory)
Challenge:
Input tile requires too much shared memory
(hurts occupancy or even exceeds limit)
Challenge:
Maximum threads per block exceeded

## Slide 23
Thread Coarsening and Tile Slicing
output
inputtile
(in shared memory)
Solution:
Assign enough threads for loading one input plane and processing one output plane
Challenge:
Input tile requires too much shared memory
(hurts occupancy or even exceeds limit)

## Slide 24
Thread Coarsening and Tile Slicing
output
inputtile
(in shared memory)
Solution:
Only store the three input planes needed by the output plane at a time
Solution:
Assign enough threads for loading one input plane and processing one output plane

## Slide 25
Thread Coarsening and Tile Slicing
output
inputtile
(in shared memory)
Solution:
Only store the three input planes needed by the output plane at a time
Solution:
Assign enough threads for loading one input plane and processing one output plane

## Slide 26
Thread Coarsening and Tile Slicing
output
inputtile
(in shared memory)
Solution:
Only store the three input planes needed by the output plane at a time
Solution:
Assign enough threads for loading one input plane and processing one output plane

## Slide 27
Thread Coarsening and Tile Slicing
output
inputtile
(in shared memory)
Solution:
Only store the three input planes needed by the output plane at a time
Solution:
Assign enough threads for loading one input plane and processing one output plane

## Slide 28
Stencil with Thread Coarsening Code
__global__ void stencil_kernel(float* in, float* out, unsigned int N) {
int iStart = blockIdx.z*OUT_TILE_DIM;
int j = blockIdx.y*OUT_TILE_DIM + threadIdx.y - 1;
int k = blockIdx.x*OUT_TILE_DIM + threadIdx.x - 1;
__shared__ float inPrev_s[IN_TILE_DIM][IN_TILE_DIM];
__shared__ float inCurr_s[IN_TILE_DIM][IN_TILE_DIM];
__shared__ float inNext_s[IN_TILE_DIM][IN_TILE_DIM];
if(iStart - 1 >= 0 && iStart - 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inPrev_s[threadIdx.y][threadIdx.x] = in[(iStart - 1)*N*N + j*N + k];
}
if(iStart >= 0 && iStart < N && j >= 0 && j < N && k >= 0 && k < N) {
inCurr_s[threadIdx.y][threadIdx.x] = in[iStart*N*N + j*N + k];
}
for(int i = iStart; i < iStart + OUT_TILE_DIM; ++i) {
if(i + 1 >= 0 && i + 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inNext_s[threadIdx.y][threadIdx.x] = in[(i + 1)*N*N + j*N + k];
}
__syncthreads();
if(i >= 1 && i < N - 1 && j >= 1 && j < N - 1 && k >= 1 && k < N - 1) {
if(threadIdx.y >= 1 && threadIdx.y < IN_TILE_DIM - 1
&& threadIdx.x >= 1 && threadIdx.x < IN_TILE_DIM - 1) {
out[i*N*N + j*N + k] = C0*inCurr_s[threadIdx.y][threadIdx.x]
+ C1*inCurr_s[threadIdx.y][threadIdx.x - 1]
+ C2*inCurr_s[threadIdx.y][threadIdx.x + 1]
+ C3*inCurr_s[threadIdx.y - 1][threadIdx.x]
+ C4*inCurr_s[threadIdx.y + 1][threadIdx.x]
+ C5*inPrev_s[threadIdx.y][threadIdx.x] +
+ C6*inNext_s[threadIdx.y][threadIdx.x];
}
}
__syncthreads();
inPrev_s[threadIdx.y][threadIdx.x] = inCurr_s[threadIdx.y][threadIdx.x];
inCurr_s[threadIdx.y][threadIdx.x] = inNext_s[threadIdx.y][threadIdx.x];
}
}

## Slide 29
Unshared Slices
inPrev_s
inCurr_s
inNext_s
Observation: Only the current slice is truly shared by the threads. The previous and next slice elements are only needed by the thread that loaded them.
output
inputtile
(in shared memory)
These input elements are only used with this input element

## Slide 30
Register Tiling
inPrev_s
inCurr_s
inNext_s
Optimization: Save shared memory by putting the next slice elements in registers, moving them to shared memory when they become the current slice, then moving them back to registers when they become the previous slice. We only need enough shared memory for one slice
The registers of the different threads collectively form a tile (called register tiling).
output
inputtile
(in shared memory)
These input elements are only used with this input element

## Slide 31
Stencil with Thread Coarsening Code
__global__ void stencil_kernel(float* in, float* out, unsigned int N) {
int iStart = blockIdx.z*OUT_TILE_DIM;
int j = blockIdx.y*OUT_TILE_DIM + threadIdx.y - 1;
int k = blockIdx.x*OUT_TILE_DIM + threadIdx.x - 1;
__shared__ float inPrev_s[IN_TILE_DIM][IN_TILE_DIM];
__shared__ float inCurr_s[IN_TILE_DIM][IN_TILE_DIM];
__shared__ float inNext_s[IN_TILE_DIM][IN_TILE_DIM];
if(iStart - 1 >= 0 && iStart - 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inPrev_s[threadIdx.y][threadIdx.x] = in[(iStart - 1)*N*N + j*N + k];
}
if(iStart >= 0 && iStart < N && j >= 0 && j < N && k >= 0 && k < N) {
inCurr_s[threadIdx.y][threadIdx.x] = in[iStart*N*N + j*N + k];
}
for(int i = iStart; i < iStart + OUT_TILE_DIM; ++i) {
if(i + 1 >= 0 && i + 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inNext_s[threadIdx.y][threadIdx.x] = in[(i + 1)*N*N + j*N + k];
}
__syncthreads();
if(i >= 1 && i < N - 1 && j >= 1 && j < N - 1 && k >= 1 && k < N - 1) {
if(threadIdx.y >= 1 && threadIdx.y < IN_TILE_DIM - 1
&& threadIdx.x >= 1 && threadIdx.x < IN_TILE_DIM - 1) {
out[i*N*N + j*N + k] = C0*inCurr_s[threadIdx.y][threadIdx.x]
+ C1*inCurr_s[threadIdx.y][threadIdx.x - 1]
+ C2*inCurr_s[threadIdx.y][threadIdx.x + 1]
+ C3*inCurr_s[threadIdx.y - 1][threadIdx.x]
+ C4*inCurr_s[threadIdx.y + 1][threadIdx.x]
+ C5*inPrev_s[threadIdx.y][threadIdx.x]
+ C6*inNext_s[threadIdx.y][threadIdx.x];
}
}
__syncthreads();
inPrev_s[threadIdx.y][threadIdx.x] = inCurr_s[threadIdx.y][threadIdx.x];
inCurr_s[threadIdx.y][threadIdx.x] = inNext_s[threadIdx.y][threadIdx.x];
}
}

## Slide 32
Stencil with Register Tiling Code
__global__ void stencil_kernel(float* in, float* out, unsigned int N) {
int iStart = blockIdx.z*OUT_TILE_DIM;
int j = blockIdx.y*OUT_TILE_DIM + threadIdx.y - 1;
int k = blockIdx.x*OUT_TILE_DIM + threadIdx.x - 1;
float inPrev;
__shared__ float inCurr_s[IN_TILE_DIM][IN_TILE_DIM];
float inNext;
if(iStart - 1 >= 0 && iStart - 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inPrev = in[(iStart - 1)*N*N + j*N + k];
}
if(iStart >= 0 && iStart < N && j >= 0 && j < N && k >= 0 && k < N) {
inCurr_s[threadIdx.y][threadIdx.x] = in[iStart*N*N + j*N + k];
}
for(int i = iStart; i < iStart + OUT_TILE_DIM; ++i) {
if(i + 1 >= 0 && i + 1 < N && j >= 0 && j < N && k >= 0 && k < N) {
inNext = in[(i + 1)*N*N + j*N + k];
}
__syncthreads();
if(i >= 1 && i < N - 1 && j >= 1 && j < N - 1 && k >= 1 && k < N - 1) {
if(threadIdx.y >= 1 && threadIdx.y < IN_TILE_DIM - 1
&& threadIdx.x >= 1 && threadIdx.x < IN_TILE_DIM - 1) {
out[i*N*N + j*N + k] = C0*inCurr_s[threadIdx.y][threadIdx.x]
+ C1*inCurr_s[threadIdx.y][threadIdx.x - 1]
+ C2*inCurr_s[threadIdx.y][threadIdx.x + 1]
+ C3*inCurr_s[threadIdx.y - 1][threadIdx.x]
+ C4*inCurr_s[threadIdx.y + 1][threadIdx.x]
+ C5*inPrev
+ C6*inNext;
}
}
__syncthreads();
inPrev = inCurr_s[threadIdx.y][threadIdx.x];
inCurr_s[threadIdx.y][threadIdx.x] = inNext;
}
}

## Slide 33
N
N
N
Have we seen register tiling before?
C = A x B
A
B
C
N
N
N

## Slide 34
Have we seen register tiling before?
Ctile = Atile x Btile
Atile
Btile
Ctile
The A and B input tiles were stored in shared memory.
The C output tile was stored in the registers of the threads collectively.
Stencil just made register tiling more apparent because the same tile was sometimes stored in registers and other times in shared memory.

## Slide 35
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.