## Slide 1
Chapter 17
Application Case Study – Iterative MRI Reconstruction

## Slide 2
Objective
To learn how to apply parallel programming techniques to an application
  Determining parallelism structure
  Loop transformations
  Memory layout considerations
  Validation

## Slide 3
Cartesian Scan Data
Spiral Scan Data
Gridding1
FFT
LS
2
(a)
(b)
(c)
Non-Cartiesian MRI Scan
More samples near origin, giving better resolution for important parts of the scan space
Notes: Thus, non-Cartesian trajectories, such as the spiral trajectory shown here, are becoming increasingly popular. These non-Cartesian scans are faster and less susceptible to artifacts than Cartesian scans.
However, the FFT cannot be applied directly to the non-Cartesian scan data. One popular approach is to “grid” the data. That is, the non-Cartesian data (shown in orange) is interpolated onto a uniform grid (shown in blue) using some sort of windowing function. The FFT can then be applied to the interpolated data. This technique introduces inaccuracies and satisfies no statistical optimality criterion, but is very fast, and does produce better images than a Cartesian scan.

## Slide 4
Compute FHF + λWHW
Acquire Data
Compute FHD
Find ρ
An Iterative Solver Based Apparch to Image Reconstruction
Notes: The least-squares reconstruction algorithm poses the reconstruction problem in the form FHF times p = FHd.
1. P is the desired image.
2. FHF is a special data structure that can be derived very quickly from another data structure, Q. Q depends only on the scanner configuration and can therefore be computed before the scan data is even acquired. So, while computing Q is very expensive, this cost can be amortized over many reconstructions, and does not factor into the reconstruction time for any image.
3. FHd is a matrix that depends on both the scanner configuration and the data. Computing FHd is fairly expensive.
Finally, given FHF and FHd, a linear solver is used to find the image. This last step is quite fast. In fact, 99.5% of the reconstruction time for a single image is devoted to computing FHd, and computing Q is even more expensive, so those are the computations that we chose to accelerate on the G80.

## Slide 5
for (m = 0; m < M; m++) {
phiMag[m] = rPhi[m]*rPhi[m] +
iPhi[m]*iPhi[m];
for (n = 0; n < N; n++) {
expQ = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
rQ[n] +=phiMag[m]*cos(expQ);
iQ[n] +=phiMag[m]*sin(expQ);
}
}
(a) Q computation
for (m = 0; m < M; m++) {
rMu[m] = rPhi[m]*rD[m] +
iPhi[m]*iD[m];
iMu[m] = rPhi[m]*iD[m] –
iPhi[m]*rD[m];
for (n = 0; n < N; n++) {
expFhD = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
cArg = cos(expFhD);
sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg –
iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg +
rMu[m]*sArg;
}
} (b) FHD computation
Computation of Q and FHD

## Slide 6
__global__ void cmpFhD(float* rPhi, iPhi, rD, iD,
kx, ky, kz, x, y, z, rMu, iMu, rFhD, iFhD, int N) {
int m = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
rMu[m] = rPhi[m]*rD[m] + iPhi[m]*iD[m];
iMu[m] = rPhi[m]*iD[m] – iPhi[m]*rD[m];
for (n = 0; n < N; n++) {
float expFhD = 2*PI*(kx[m]*x[n] + ky[m]*y[n] + kz[m]*z[n]);
float cArg = cos(expFhD); float sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg – iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg + rMu[m]*sArg;
}
}
6
First version of the FHD kernel.
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 7
for (m = 0; m < M; m++) {
rMu[m] = rPhi[m]*rD[m] +
iPhi[m]*iD[m];
iMu[m] = rPhi[m]*iD[m] –
iPhi[m]*rD[m];
for (n = 0; n < N; n++) {
expFhD = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
cArg = cos(expFhD);
sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg –
iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg +
rMu[m]*sArg;
}
}
(a) FHD computation
for (m = 0; m < M; m++) {
rMu[m] = rPhi[m]*rD[m] +
iPhi[m]*iD[m];
iMu[m] = rPhi[m]*iD[m] –
iPhi[m]*rD[m];
}
for (m = 0; m < M; m++) {
for (n = 0; n < N; n++) {
expFhD = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
cArg = cos(expFhD);
sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg –
iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg +
rMu[m]*sArg;
}
} (b) after loop fission
Loop Fission

## Slide 8
__global__ void cmpMu(float* rPhi, iPhi, rD, iD, rMu, iMu)
{
int m = blockIdx.x * MU_THREAEDS_PER_BLOCK + threadIdx.x;
rMu[m] = rPhi[m]*rD[m] + iPhi[m]*iD[m];
iMu[m] = rPhi[m]*iD[m] – iPhi[m]*rD[m];
}
cmpMu kernel

## Slide 9
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
kx, ky, kz, x, y, z, rMu, iMu, int N) {
int m = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
for (n = 0; n < N; n++) {
float expFhD = 2*PI*(kx[m]*x[n]+ky[m]*y[n]+kz[m]*z[n]);
float cArg = cos(expFhD);
float sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg – iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg + rMu[m]*sArg;
}
}
6
Second option of the FHD kernel
Notes: The algorithms for Q and FhD are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 10
for (m = 0; m < M; m++) {
for (n = 0; n < N; n++) {
expFhD = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
cArg = cos(expFhD);
sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg –
iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg +
rMu[m]*sArg;
}
} (a) before loop interchange
for (n = 0; n < N; n++) {
for (m = 0; m < M; m++) {
expFhD = 2*PI*(kx[m]*x[n] +
ky[m]*y[n] +
kz[m]*z[n]);
cArg = cos(expFhD);
sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg –
iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg +
rMu[m]*sArg;
}
} (b) after loop interchange
Loop interchange of the FHD computation

## Slide 11
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
kx, ky, kz, x, y, z, rMu, iMu, int M) {
int n = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
for (m = 0; m < M; m++) {
float expFhD = 2*PI*(kx[m]*x[n]+ky[m]*y[n]+kz[m]*z[n]);
float cArg = cos(expFhD);
float sArg = sin(expFhD);
rFhD[n] += rMu[m]*cArg – iMu[m]*sArg;
iFhD[n] += iMu[m]*cArg + rMu[m]*sArg;
}
}
6
Third option of the FHD kernel
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 12
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
kx, ky, kz, x, y, z, rMu, iMu, int M) {
int n = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
float xn_r = x[n]; float yn_r = y[n]; float zn_r = z[n];
float rFhDn_r = rFhD[n]; float iFhDn_r = iFhD[n];
for (m = 0; m < M; m++) {
float expFhD = 2*PI*(kx[m]*xn_r+ky[m]*yn_r+kz[m]*zn_r);
float cArg = cos(expFhD);
float sArg = sin(expFhD);
rFhDn_r += rMu[m]*cArg – iMu[m]*sArg;
iFhDn_r += iMu[m]*cArg + rMu[m]*sArg;
}
rFhD[n] = rFhD_r; iFhD[n] = iFhD_r;
}
6
Using registers to reduce memory accesses in the FHD kernel
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 13
__constant__ float kx_c[CHUNK_SIZE],
ky_c[CHUNK_SIZE], kz_c[CHUNK_SIZE];
…
__ void main() {
int i;
for (i = 0; i < M/CHUNK_SIZE; i++);
cudaMemcpyToSymbol(kx_c,&kx[i*CHUNK_SIZE],4*CHUNK_SIZE, cudaMemCpyHostToDevice);
cudaMemcpyToSymbol(ky_c,&ky[i*CHUNK_SIZE],4*CHUNK_SIZE, cudaMemCpyHostToDevice);
cudaMemcpyToSymbol(ky_c,&ky[i*CHUNK_SIZE],4*CHUNK_SIZE, cudaMemCpyHostToDevice);
…
cmpFhD<<<FHD_THREADS_PER_BLOCK, N/FHD_THREADS_PER_BLOCK>>> (rPhi, iPhi, phiMag, x, y, z, rMu, iMu, CHUNK_SIZE);
}
/* Need to call kernel one more time if M is not */
/* perfect multiple of CHUNK SIZE */
}
6
Chunking k-space data to fit into constant memory
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 14
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
x, y, z, rMu, iMu, int M) {
int n = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
float xn_r = x[n]; float yn_r = y[n]; float zn_r = z[n];
float rFhDn_r = rFhD[n]; float iFhDn_r = iFhD[n];
for (m = 0; m < M; m++) {
float expFhD = 2*PI*(kx_c[m]*xn_r+ky_c[m]*yn_r+kz_c[m]*zn_r);
float cArg = cos(expFhD);
float sArg = sin(expFhD);
rFhDn_r += rMu[m]*cArg – iMu[m]*sArg;
iFhDn_r += iMu[m]*cArg + rMu[m]*sArg;
}
rFhD[n] = rFhD_r; iFhD[n] = iFhD_r;
}
6
Revised FHD Kernel – Constant Memory
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 15
25
(a) k-space data stored in separate arrays.
(b) k-space data stored in an array whose elements are structs.
Constant Memory Layout Consideration
Storing k-space samples in three separate arrays requires 3 cache lines for each warp
  Interleaving x, y, z values of the same sample in the same array reduces the cache line requirement to 1 per warp
Notes: How can the layout of scan data in the constant memory be causing the poor performance we just observed?
First, recall that the kx, ky, kz, and phi components of the same scan point have both temporal and spatial locality.
The temporal locality is across threads (when one thread loads a scan point, there’s a high probability that another thread will load the same scan point soon).
The spatial locality is both within and across threads (when one thread loads a scan point, there’s a high probability that the same thread and other threads will load nearby scan points soon).
In the old data layout, the components of the same scan point are not in contiguous memory. So prefetching isn’t as effective as it might be, and in-phase threads may cause a lot of unnecessary cache conflicts, depending on the line size and associativity of the constant caches.
In the new data layout, those problems don’t exist.

## Slide 16
struct kdata {
float x, float y, float z;
} k;
__constant__ struct kdata k_c[CHUNK_SIZE];
…
__ void main() {
int i;
for (i = 0; i < M/CHUNK_SIZE; i++);
cudaMemcpyToSymbol(k_c,k,12*CHUNK_SIZE, cudaMemCpyHostToDevice);
cmpFhD<<<FHD_THREADS_PER_BLOCK, N/FHD_THREADS_PER_BLOCK>>> (…);
}
}
6
Host Code with Adjusted Constant Memory Layout
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 17
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
x, y, z, rMu, iMu, int M) {
int n = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
float xn_r = x[n]; float yn_r = y[n]; float zn_r = z[n];
float rFhDn_r = rFhD[n]; float iFhDn_r = iFhD[n];
for (m = 0; m < M; m++) {
float expFhD = 2*PI*(k[m].x*xn_r+k[m].y*yn_r+k[m].z*zn_r);
float cArg = cos(expFhD);
float sArg = sin(expFhD);
rFhDn_r += rMu[m]*cArg – iMu[m]*sArg;
iFhDn_r += iMu[m]*cArg + rMu[m]*sArg;
}
rFhD[n] = rFhD_r; iFhD[n] = iFhD_r;
}
6
Adjusted k-space data constant memory layout in the FHD kernel
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 18
__global__ void cmpFhD(float* rPhi, iPhi, phiMag,
x, y, z, rMu, iMu, int M) {
int n = blockIdx.x * FHD_THREADS_PER_BLOCK + threadIdx.x;
float xn_r = x[n]; float yn_r = y[n]; float zn_r = z[n];
float rFhDn_r = rFhD[n]; float iFhDn_r = iFhD[n];
for (m = 0; m < M; m++) {
float expFhD = 2*PI*(k[m].x*xn_r+k[m].y*yn_r+k[m].z*zn_r);
float cArg = __cos(expFhD);
float sArg = __sin(expFhD);
rFhDn_r += rMu[m]*cArg – iMu[m]*sArg;
iFhDn_r += iMu[m]*cArg + rMu[m]*sArg;
}
rFhD[n] = rFhD_r; iFhD[n] = iFhD_r;
}
6
Using Hardware __sin() and __cos()
Notes: The algorithms for Q and FHd are nearly identical, so in the interest of time we’ll examine only Q.
There are M scan points, with the 3D scan data represented by kx, ky, kz, and phi.
There are N pixels, with the 3D pixel data represented by x, y, and z (inputs) and Q (output).
As you can see, the algorithm is embarrassingly data-parallel.
Each iteration of the outer loop corresponds to a single point of scan data. For that single point of scan data, we first compute the magnitude-squared of phi. Then, the inner loop iterates over all the pixels, because the current scan data point contributes to the value of Q at every pixel. In other words, the value of Q at each pixel depends on every scan point. Clearly, the algorithm is O(MN).
Examining the inner loop more closely, we see that there are 10 floating-point arithmetic operations, 2 floating-point trig operations, and 10 loads. This instruction mix hints at the bottlenecks we face as we map this algorithm to the G80.

## Slide 19
20
A.N. Netravali and B.G. Haskell, Digital Pictures: Representation, Compression, and Standards (2nd Ed), Plenum Press, New York, NY (1995).
I0 is a known, “perfect” answer. This is typically done by creating k-space samples for a known image, producing a reconstructed image, and compare the two.
Validating Reconstructed Image Using Signal-to-Noise Ratio

## Slide 20
Validation of floating-point
precision and accuracy of the different
FHD implementations.
Is the known image answer
(sometimes called a phantom image)
Note that all GPU optimized versions have comparable PSNR as (3) the CPU double-precision version

## Slide 21
30
Component and Whole-Application Speedup
 | Q |  | FHD |  | Total | 
Reconstruction | Run Time (m) | GFLOP | Run Time (m) | GFLOP | Linear Solver (m) | Recon. Time (m)
Gridding + FFT (CPU, DP) | N/A | N/A | N/A | N/A | N/A | 0.39
LS (CPU, DP) | 4009.0 | 0.3 | 518.0 | 0.4 | 1.59 | 519.59
LS (CPU, SP) | 2678.7 | 0.5 | 342.3 | 0.7 | 1.61 | 343.91
LS (GPU, Naïve) | 260.2 | 5.1 | 41.0 | 5.4 | 1.65 | 42.65
LS (GPU, CMem) | 72.0 | 18.6 | 9.8 | 22.8 | 1.57 | 11.37
LS (GPU, CMem, SFU, Exp) | 7.5 | 178.9 | 1.5 | 144.5 | 1.69 | 3.19
108X
228X
357X
Notes: Also, relative to the CPU, the GPU achieves speedup of 357X for Q, 228X for FHd, and 108X for the reconstruction.
The acceleration for FHd is lower than the acceleration for Q most likely because FHd has two sines and two cosines in each inner loop, which may oversubscribe the SFUs.
The acceleration for the total reconstruction is only 108X because the linear solver, which initially accounted for less than 0.5% of the reconstruction, now accounts for roughly 50%. We expect that the running the solver on the G80 will cut the total reconstruction time to about 100 seconds.

## Slide 22
References
Wen-mei W. Hwu, David B. Kirk, and Izzat El Hajj. Programming Massively Parallel Processors: A Hands-on Approach. Morgan Kaufmann, 2022.